## Slide 1: I/O Devices
CSE 13S
Prof. Darrell Long
IO, IO, use <stdio.h> that’s how to code in Unix you know, IO, IO, …
Bonus
Lecture

## Slide 2: Input/Output
Principles of I/O hardware
Principles of I/O software
I/O software layers
Disks
Clocks
Character-oriented terminals
Graphical user interfaces
Network terminals
Power management

## Slide 3: How fast is I/O hardware?
Device | Data rate (typical)
Keyboard | 10 bytes/sec
Mouse | 100 bytes/sec
56K modem | 7 KB/sec
Printer / scanner | 1 MB/sec
USB | 1.5 / 60 / 625 MB/sec
Digital camcorder | 4 MB/sec
Gigabit Ethernet | 125 MB/sec
Hard drive | 125 MB/sec
Flash drive (SSD) | 200 MB/sec
DisplayPort | 1.62 / 2.7 / 5.4 / 8.1 Gbit/s per lane data rate per lane; 1, 2, or 4 lane
PCIe bus | 985 MB/sec per lane
Notes: Up to 16 lanes for PCIe.
1-4 lanes for DisplayPort

## Slide 4: Device controllers
I/O devices have components
  Mechanical component
  Electronic component
Electronic component controls the device
  May be able to handle multiple devices
  May be more than one controller per mechanical component (example: hard drive)
Controller's tasks
  Convert serial bit stream to block of bytes
  Perform error correction as necessary
  Make available to main memory

## Slide 5: How is memory-mapped I/O done?
Single-bus
  All memory accesses go over a shared bus
  I/O and RAM accesses compete for bandwidth
Dual-bus
  RAM access over high-speed bus
  I/O access over lower-speed bus
  Less competition for bus
  More hardware (more expensive…)
CPU
Memory
I/O
This port allows I/O devices access into memory
Memory
I/O
CPU

## Slide 6: Direct Memory Access (DMA)
CPU
DMA
controller
Disk
controller
Main
memory
Address
Count
Control
1: CPU programs the DMA controller
2: DMA controller requests transfer to memory
Buffer
3: Data is transferred
4: ACK
5: Interrupt when done

## Slide 7: Hardware’s view of interrupts
Bus
1. Device finishes
2. Controller issues interrupt
3. CPU ACKs interrupt
CPU
Interrupt controller

## Slide 8: I/O software: goals
Device independence
  Programs can access any I/O device
  No need to specify device in advance
Uniform naming
  Name of a file or device is a string or an integer
  Doesn’t depend on the machine (underlying hardware)
Error handling
  Done as close to the hardware as possible
  Isolate higher-level software
Synchronous vs. asynchronous transfers
  Blocked transfers vs. interrupt-driven
Buffering
  Data coming off a device cannot be stored in final destination
Sharable vs. dedicated devices

## Slide 9: Programmed I/O: printing a page
Printed page
ABCD EFGH
Kernel
User
A
Printed page
ABCD EFGH
ABCD EFGH
AB
Printed page
ABCD EFGH
ABCD EFGH

## Slide 10: Code for programmed I/O
copy_from_user (buffer, p, count); // copy into kernel buffer
for (j = 0; j < count; j++) { // loop for each char
// wait for printer to be ready while (*printer_status_reg != READY) ; // output a single character *printer_data_reg = p[j];
}
return_to_user();

## Slide 11: Interrupt Driven I/O
Run by system call
Run by interrupt
copy_from_user (buffer, p, count);
j = 0;
enable_interrupts();
while (*printer_status_reg != READY) ;
*printer_data_reg = p[0];
scheduler(); // and block user
if (count == 0) { unblock_user();
} else { *printer_data_reg = p[j]; count--; j++;
}
acknowledge_interrupt();
return_from_interrupt();

## Slide 12: Layers of I/O software
Operating system (kernel)
User
Hardware
Interrupt handlers
Device drivers
Device-independent OS code
User software & libraries
Notes: Start here on Wed 5/6.

## Slide 13: Interrupt handlers
Interrupt handlers are best hidden
  Driver starts an I/O operation and blocks
  Interrupt notifies of completion
Interrupt procedure does its task
  Then unblocks driver that started it
  Perform minimal actions at interrupt time
    Some of the functionality can be done by the driver after it is unblocked
Interrupt handler must
  Save registers not already saved by interrupt hardware
  Set up context for interrupt service procedure

## Slide 14: What happens on an interrupt
Set up the stack for interrupt service procedure
Ack interrupt controller, reenable interrupts
Copy registers from where saved
Run service procedure
(optional) Pick a new process to run next
Set up MMU context for process to run next
Load new process’ registers
Start running the new process

## Slide 15: Device drivers
Device drivers go between device controllers and rest of OS
  Drivers standardize interface to widely varied devices
Device drivers communicate with controllers over bus
  Controllers communicate with devices themselves
Kernel space
user program
Keyboard driver
Rest of the OS
Keyboard controller
Disk drive controller
Disk drive driver

## Slide 16: Device-independent I/O software
Device-independent I/O software provides common “library” routines for I/O software
Helps drivers maintain a standard appearance to the rest of the OS
Uniform interface for many device drivers for
  Buffering
  Error reporting
  Allocating and releasing dedicated devices
  Suspending and resuming processes
Common resource pool
  Device-independent block size (keep track of blocks)
  Other device driver resources

## Slide 17: Why a standard driver interface?
Non-standard device driver interface
  Different interface for each driver
  High OS complexity
  Less code reuse
Standard device driver interface
Less OS/driver interface code
Lower OS complexity
Easy to add new drivers
Operating system
Operating system

## Slide 18: Buffering device input
User space
Kernel space
User space
Kernel space
User space
Kernel space
User space
Kernel space
Unbuffered input
Buffering in user space
Buffer in kernel Copy to user space
Double buffer in kernel

## Slide 19: What happens where on an I/O request?
User processes
Device-independent code
Device drivers
Interrupt handlers
Hardware
Request
Reply
Make I/O call; format I/O; spooling
Naming, protection blocking / buffering / allocation
Manage device registers & status
Signal device driver on completed I/O
Actually do the I/O (in hardware)

## Slide 20: Disk drive structure
Data stored on surfaces
  Up to two surfaces per platter
  One or more platters per disk
Data in concentric tracks
  Tracks broken into sectors
    256B–4KB per sector
  Cylinder: corresponding tracks on all surfaces
Data read and written by heads
  Actuator moves heads
  Heads move in unison
actuator
surfaces
sector
cylinder
platter
spindle
track
head

## Slide 21: Disk drive specifics
 | IBM 360KB floppy | Seagate 3 TB HD
Cylinders | 40 | 240,000 (estimate)
Tracks per cylinder | 2 | 10
Sectors per track | 9 | 2500 (average)
Sectors per disk | 720 | 6 × 109
Bytes per sector | 512 | 512
Capacity | 360 KB | 3 TB
Seek time (minimum) | 6 ms | 1.5 ms (?)
Seek time (average) | 77 ms | 4.16 ms
Rotation time | 200 ms | 8.3 ms
Spinup time | 250 ms | ~5 sec (?)
Sector transfer time | 22 ms | 3.4 μsec

## Slide 22: Structure of a disk sector
Preamble contains information about the sector
  Sector number & location information
Data is usually 512 or 1024 bytes
  Newer disks moving to 4KB sectors
ECC (Error Correcting Code) is used to detect & correct minor errors in the data
Preamble
Data
ECC

## Slide 23: Sector layout on disk
Sectors numbered sequentially on each track
Numbering starts in different place on each track: sector skew
  Allows time for switching head from track to track
  Done to minimize delay in sequential transfers
Zoning
  Different zones have different number of sectors per track
  Outer zones have higher transfer rate
  Typically 8–30 zones (or more)
  Zones set at time of manufacture

## Slide 24: Disk Addressing
Millions of sectors on the disk must be labeled
Two possibilities
  Cylinder/track/sector
  Sequential numbering
Modern drives use sequential numbers
  Disks map sequential numbers into specific location
  Mapping may be modified by the disk
    Remap bad sectors
    Optimize performance
  Hide the exact geometry, making life simpler for the OS

## Slide 25: When good disks go bad…
Disks have defects
  With billions of sectors, this isn’t surprising!
ECC helps with errors, but sometimes this isn’t enough
Disks keep spare sectors (normally unused) and remap bad sectors into these spares
  If there’s time, the whole track could be reordered…
All of this is transparent to the user (and, typically, OS)

## Slide 26: Building a better disk
Problem: CPU performance has been increasing exponentially, but disk performance hasn’t
  Disks are limited by mechanics
Problem: disks aren’t all that reliable
Solution: distribute data across disks, and use some of the space to improve reliability
  Data transferred in parallel
  Data stored across drives (striping)
Problem: more disks means less reliability
  Generate & store additional information to allow data from a failed disk to be recovered

## Slide 27: Calculating parity
Goal: keep extra information to recover from device failure
Use the extra information to rebuild the data on the missing device
There are formulas to recover from more than one failure with additional “parity” devices
D0 ⊕ D1 ⊕ D2 ⊕ D3 = P
D0 ⊕ D1 ⊕ D2 ⊕ D3 = P
⊕ (D2 ⊕ P)
⊕ (D2 ⊕ P)
D0 ⊕ D1 ⊕ D3 ⊕ P = D2
Notes: Suppose D2 fails. How do we recover it?
Note that we need to know that D2 is the disk that failed; this doesn’t work if we don’t know where the failure is.
Can we recover from more than one failure? Yes, if we have more than one parity disk (and a different formula).

## Slide 28: What’s in a disk request?
Time required to read or write a disk block determined by 3 factors
  Seek time
    Typically around 2–8 ms, depending on distance
    Longer seeks take longer, but not linear with distance
  Rotational delay
    Average delay = 1/2 rotation time
    Example: rotate in 10 ms, average rotation delay = 5 ms
  Actual transfer time
    Transfer time = time to rotate over sector
    Example: rotate in 10 ms, 1000 sectors/track ⇒ 10/1000 ms = 0.01 ms (10 μs) transfer time per sector
Seek time and rotation time comparable
Error checking is done by on-disk controller
Notes: Cover disk requests on Monday 5/11. Then skip past flash.

## Slide 29: Disk request scheduling
Goal: use disk hardware efficiently
  Bandwidth as high as possible
  Disk transferring as often as possible (and not seeking)
We want to
  Minimize disk seek time (moving from track to track)
  Minimize rotational latency (waiting for disk to rotate the desired sector under the read/write head)
Calculate disk bandwidth by
  Total bytes transferred / time to service request
  Seek time & rotational latency are overhead (no data is transferred), and reduce disk bandwidth
Minimize seek time & rotational latency by
  Using algorithms to find a good sequence for servicing requests
  Placing blocks of a given file “near” each other

## Slide 30: Disk scheduling algorithms
Schedule disk requests to minimize disk seek time
  Seek time increases as distance increases (though not linearly)
  Minimize seek distance ➔ minimize seek time
Disk seek algorithm examples assume a request queue & head position (disk has 200 cylinders)
  Queue = 100, 175, 51, 133, 8, 140, 73, 77
  Head position = 63

## Slide 31: First-Come-First Served (FCFS)
Requests serviced in the order in which they arrived
  Easy to implement!
  May involve lots of unnecessary seek distance
Seek order = 100, 175, 51, 133, 8, 140, 73, 77
Seek distance = (100-63) + (175-100) + (175-51) + (133-51) + (133-8) + (140-8) + (140-73) + (77-73) = 646 cylinders

## Slide 32: Shortest Seek Time First (SSTF)
Service the request with the shortest seek time from the current head position
  Form of SJF scheduling
  May starve some requests
Seek order = 73, 77, 51, 8, 100, 133, 140, 175
Seek distance = 10 + 4 + 26 + 43 + 92 + 33 + 7 + 35 = 250 cylinders

## Slide 33: SCAN (elevator algorithm)
Disk arm starts at one end of the disk and moves towards the other end, servicing requests as it goes
  Reverses direction when it gets to end of the disk
  Also known as elevator algorithm
Seek order = 51, 8, 0 , 73, 77, 100, 133, 140, 175
Seek distance = 12 + 43 + 8 + 73 + 4 + 23 + 33 + 7 + 35 = 238 cylinders

## Slide 34: C-SCAN
Identical to SCAN, except head returns to cylinder 0 when it reaches the end of the disk
  Treats cylinder list as a circular list that wraps around the disk
  Waiting time is more uniform for cylinders near the edge of the disk
Seek order = 73, 77, 100, 133, 140, 175, 199, 0, 8, 51
Distance = 10 + 4 + 23 + 33 + 7 + 35 + 24 + 199 + 8 + 43 = 386 cyls

## Slide 35: C-LOOK
Identical to C-SCAN, except head only travels as far as the last request in each direction
  Saves seek time from last sector to end of disk
Seek order = 73, 77, 100, 133, 140, 175, 8, 51
Distance = 10 + 4 + 23 + 33 + 7 + 35 + 167 + 43 = 322 cylinders

## Slide 36: Picking a disk scheduling algorithm
SSTF is easy to implement and works OK if there aren’t too many disk requests in the queue
SCAN-type algorithms perform better for systems under heavy load
  More fair than SSTF
  Use LOOK rather than SCAN algorithms to save time
Long seeks aren’t too expensive, so choose C-LOOK over LOOK to make response time more even
Disk request scheduling interacts with algorithms for allocating blocks to files
  Make scheduling algorithm modular: allow it to be changed without changing the file system
Use SSTF or FCFS for lightly loaded systems
Use C-LOOK for heavily loaded systems

## Slide 37: Flash memory (and SSDs)
Compared to disk, flash is
  Faster (shorter access time, but lower bandwidth)
  More expensive
  More reliable (devices)
  Less reliable (sectors)
Compared to DRAM, flash is
  Cheaper (a bit)
  Non-volatile (data survives power loss)
  Slower
Use flash as a level between disk and memory?
Issues
  Can’t overwrite sectors “in place”
  Flash wears out: can only write 3,000–100,000 times per memory cell

## Slide 38: Writing to flash memory
Can’t overwrite page in place
  Need to write to “clean” region
  Unit of erase is “erase block”
One solution: copy entire erase block to new location
  Modify the page being written
This isn’t efficient!
  Flash vendors spend a lot of time on Flash Translation Layers
  FTLs map logical page numbers to physical pages
  Also manage wear leveling: distribute erases among blocks

## Slide 39: Handling flash in the OS
Treat it like a disk?
  Flash is written in blocks, just like a disk
    Blocks have to be erased first: somewhat slow
    Erase blocks are much larger than pages
  Flash is random access, just like a disk
  This approach is often used!
Need to be careful about wearing out flash
  Most flash devices do “wear leveling”: remap blocks internally when they’re erased
  File systems for flash should take wear into account
    Many don’t, including the standard VFAT file system

## Slide 40: Clock hardware
Crystal oscillator with fixed frequency (only when computer is on)
  Typically used to time short intervals (~ 1 second)
  May be used to correct time-of-day clock
Time-of-day clock (runs when system is off)
  Keeps minutes, hours, days
  May not be too accurate…
  Used to load system clock at startup
Time kept in seconds and ticks (often 102–106 per second)
  Number of seconds since a particular time
    For many versions of Unix, tick 0 was on January 1, 1970
  Number of ticks this second
  Advance ticks once per clock interrupt
  Advance seconds when ticks “overflow”
Notes: Start here on Monday 5/11, but cover disk scheduling first.

## Slide 41: Keeping time
Check time via the Web
  Protocol to get time from accurate time servers (ntp)
What happens when system clock is slow?
  Advance clock to the correct current time
  May be done all at once or over a minute or two
What happens when system clock is fast?
  Can’t have time run backwards!
  Instead, advance time more slowly than normal until the clock is correct
Track clock drift, do periodic updates to keep clock accurate

## Slide 42: Using timers in software
Use short interval clock for timer interrupts
  Specified by applications
  No problems if interrupt frequency is low
  May have multiple timers using a single clock chip
Use soft timers to avoid interrupts
  Kernel checks for soft timer expiration before it exits to user mode
  Less accurate than using a hardware timer
  How well this works depends on rate of kernel entries
Notes: Start here on Thursday 5/14.

## Slide 43: Where does the power go?
How much power does each part of a laptop computer use?
  Display is the biggest energy hog, by far!
  Chipset (including memory) is next
Save power by
  Reducing display power
    Turning down the backlight
  Slowing down CPU
  Using “less” of the CPU
  Using an alternate GPU
  Powering down hard drive
  Using a flash-based drive
Source: http://blogs.msdn.com/b/e7/archive/2009/01/06/windows-7-energy-efficiency.aspx

## Slide 44: Reducing CPU power usage
Running at full clock speed
  Jobs finish quickly
  High energy consumption: proportional to shaded area
  Intel processors may use 50–75 watts!
Cutting voltage by two
  Cuts clock speed by two: processes take longer
  Cuts power by four
  Cuts energy consumption (= power × time) in half

## Slide 45: How can we reduce power usage?
Tell the programs to use less energy
  May mean poorer user experience
  Makes batteries last longer!
Examples
  Dim the screen
  Switch to lower-power processor modes
    Dynamic voltage scaling for the CPU
    Shut down CPU cores
    Use a lower-power GPU
  Fewer image updates per second (one reason why Kindle is so power efficient)
  Use application-specific chips (Apple M7/M8 for motion capture)
Notes: Kindle actually uses e-Ink.